## Slide 1: ECE408/CS483/CSE408 Spring 2018 Applied Parallel Programming Lectures 4: Memory Model

## Slide 2: Objective
To learn the basic features of the memories accessible by CUDA threads
To prepare for MP-2 - basic matrix multiplication
To learn to evaluate the performance implications of global memory accesses

## Slide 3: Programmer View of CUDA Memories
Each thread can:
  Read/write per-thread registers (~1 cycle)
  Read/write per-block shared memory (~5 cycles)
  Read/write per-grid global memory (~500 cycles)
  Read/only per-grid constant memory (~5 cycles with caching)
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 4: The Von-Neumann Model
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 5: Going back to the program
Every instruction needs to be fetched from memory, decoded, then executed.
  The decode stage typically accesses register file
Instructions come in three flavors: Operate, Data transfer, and Program Control Flow.
An example instruction cycle is the following:
Fetch | Decode | Execute | Memory
Notes: victoria@samsung.com

## Slide 6: Operate Instructions
Example of an operate instruction:
ADD R1, R2, R3
R1 – dest, R2, R3 - src
Instruction cycle for an operate instruction:
Fetch | Decode | Execute | Memory

## Slide 7: Memory Access Instructions
Examples of memory access instruction:
LDR R1, R2, #2
STR R1, R2, #2
Instruction cycle for an operate instruction:
Fetch | Decode | Execute | Memory

## Slide 8: Registers vs Memory
Registers are “free”
  No additional memory access instruction
  Very fast to use, however, there are very few of them
Memory is expensive (slow), but very large
Notes: Desk analogy: books on your desk are registers. The library is memory

## Slide 9: CUDA Variable Type Qualifiers
__device__ is optional when used with __shared__, or __constant__
Automatic variables without any qualifier reside in a register
  Except per-thread arrays that reside in global memory
Variable declaration | Memory | Scope | Lifetime
int LocalVar; | register | thread | thread
__device__ __shared__ int SharedVar; | shared | block | block
__device__ int GlobalVar; | global | grid | application
__device__ __constant__ int ConstantVar; | constant | grid | application

## Slide 10: Matrix Multiplication Example A Simple Host Version in C
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
// Matrix multiplication on the (CPU) host in single precision
void MatrixMulOnHost(float* M, float* N, float* P, int Width)‏
{
for (int i = 0; i < Width; ++i)‏
for (int j = 0; j < Width; ++j) {
float sum = 0;
for (int k = 0; k < Width; ++k) {
float a = M[i * Width + k];
float b = N[k * Width + j];
sum += a * b;
}
P[i * Width + j] = sum;
}
}
i
k
k
j
Notes: Point out that I and j will become global thread indices.

## Slide 11: Kernel Function - A Small Example
Have each 2D thread block to compute a (TILE_WIDTH)2 sub-matrix (tile) of the result matrix
  Each has (TILE_WIDTH)2 threads
Generate a 2D Grid of (WIDTH/TILE_WIDTH)2 blocks
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P2,3
P3,3
P3,1
Block(0,0)
Block(0,1)
Block(1,1)
Block(1,0)
WIDTH = 4; TILE_WIDTH = 2
Each block has 2*2 = 4 threads
WIDTH/TILE_WIDTH = 2
Use 2* 2 = 4 blocks

## Slide 12: A Slightly Bigger Example (TILE_WIDTH =2)
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
P0,5
P0,4
P1,4
P0,6
P0,7
P1,5
P2,4
P2,6
P2,7
P2,5
P1,7
P1,6
P3,4
P3,6
P3,7
P3,5
P4,1
P4,0
P5,0
P4,2
P4,3
P5,1
P6,0
P6,2
P6,3
P6,1
P5,3
P5,2
P7,0
P7,2
P7,3
P7,1
P4,5
P4,4
P5,4
P4,6
P4,7
P5,5
P6,4
P6,6
P6,7
P6,5
P5,7
P5,6
P7,4
P7,6
P7,7
P7,5
WIDTH = 8; TILE_WIDTH = 2
Each block has 2*2 = 4 threads
WIDTH/TILE_WIDTH = 4
Use 4* 4 = 16 blocks

## Slide 13: A Slightly Bigger Example (cont.) (TILE_WIDTH = 4)
WIDTH = 8; TILE_WIDTH = 4
Each block has 4*4 =16 threads
WIDTH/TILE_WIDTH = 2
Use 2* 2 = 4 blocks
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
P0,5
P0,4
P1,4
P0,6
P0,7
P1,5
P2,4
P2,6
P2,7
P2,5
P1,7
P1,6
P3,4
P3,6
P3,7
P3,5
P4,1
P4,0
P5,0
P4,2
P4,3
P5,1
P6,0
P6,2
P6,3
P6,1
P5,3
P5,2
P7,0
P7,2
P7,3
P7,1
P4,5
P4,4
P5,4
P4,6
P4,7
P5,5
P6,4
P6,6
P6,7
P6,5
P5,7
P5,6
P7,4
P7,6
P7,7
P7,5

## Slide 14: Kernel Invocation (Host-side Code)
// Setup the execution configuration
// TILE_WIDTH is a #define constant
dim3 dimGrid(ceil((1.0*Width)/TILE_WIDTH),
ceil((1.0*Width)/TILE_WIDTH), 1);
dim3 dimBlock(TILE_WIDTH, TILE_WIDTH, 1);
// Launch the device computation threads!
MatrixMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd, Width);

## Slide 15: Kernel Function
// Matrix multiplication kernel – per thread code
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)‏
{
// Pvalue is used to store the element of the matrix
// that is computed by the thread
float Pvalue = 0;

## Slide 16: Work for Block (0,0) in a TILE_WIDTH = 2 Configuration
Col = 0 * 2 + threadIdx.x
Row = 0 * 2 + threadIdx.y
Col = 0
Col = 1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
Row = 0
Row = 1
blockIdx.x
blockIdx.y
blockDim.x
blockDim.y

## Slide 17: Work for Block (0,1)
P0,1
P0,0
P0,1
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
Row = 0
Row = 1
Col = 2
Col = 3
Col = 1 * 2 + threadIdx.x
Row = 0 * 2 + threadIdx.y
blockIdx.x
blockIdx.y
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N2,3
N3,3
N3,1

## Slide 18: A Simple Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
// Calculate the row index of the d_P element and d_M
int Row = blockIdx.y*blockDim.y+threadIdx.y;
// Calculate the column idenx of d_P and d_N
int Col = blockIdx.x*blockDim.x+threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += d_M[Row*Width+k] * d_N[k*Width+Col];
d_P[Row*Width+Col] = Pvalue;
}
}

## Slide 19: How about performance on a device with 150 GB/s memory bandwidth?
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
All threads access global memory for their input matrix elements
  Two memory accesses (8 bytes) per floating point multiply-add
  4B/s of memory bandwidth/FLOPS
  150 GB/s limits the code at 37.5 GFLOPS
The actual code runs at about 25 GFLOPS
Need to drastically cut down memory accesses to get closer to the peak of more than 1,000 GFLOPS

## Slide 20: Any more questions? Read Chapter 4!