## Slide 1: ECE408/CS483/CSE408 Spring 2018 Applied Parallel Programming Lectures 5: Locality and Tiled Matrix Multiplication

## Slide 2: Objective
To learn to evaluate the performance implications of global memory accesses
To prepare for MP-3: tiled matrix multiplication

## Slide 3: Kernel Invocation (Host-side Code)
// Setup the execution configuration
// TILE_WIDTH is a #define constant
dim3 dimGrid(ceil(Width/(TILE_WIDTH*1.0)), ceil(Width/(TILE_WIDTH*1.0)), 1);
dim3 dimBlock(TILE_WIDTH, TILE_WIDTH, 1);
// Launch the device computation threads!
MatrixMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd, Width);
You need to extend the code to handle
rectangular matrix in MP-2!
X dimension

## Slide 4: A Simple Matrix Multiplication Kernel (Simplified Dimension and Syntax!)
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
// Calculate the row index of the d_P element and d_M
int Row = blockIdx.y*blockDim.y+threadIdx.y;
// Calculate the column idenx of d_P and d_N
int Col = blockIdx.x*blockDim.x+threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k){
Pvalue += d_M[Row][k] * d_N[k][Col];
}
d_P[Row][Col] = Pvalue;
}
}

## Slide 5: How about performance on a device with 150 GB/s memory bandwidth?
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
All threads access global memory for their input matrix elements
  Two memory accesses (8 bytes) per single-precision floating point multiply-add
  Two operands need to be fetched for each two floating-point operations (* and +)
  Each floating-point operation needs 4 bytes of operand
  150 GB/s limits the code at 37.5 (150/4) GFLOPS
The actual code runs at about 25 GFLOPS
Need to drastically cut down memory accesses to get closer to the peak of more than 1,000 GFLOPS

## Slide 6: Tiled Matrix-Matrix Multiplication using Shared Memory

## Slide 7: A Common Programming Strategy
Global memory is implemented with DRAM - slow
A profitable way of performing computation on the device is to tile the input data to take advantage of fast shared memory:
  Partition data into subsets (tiles) that fit into the (smaller but faster) shared memory
  Handle each data subset with one thread block by:
    Loading the subset from global memory to shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the subset from shared memory; each thread can efficiently access any data element
    Copying results from shared memory to global memory
  Tiles are also called blocks in the literature

## Slide 8: Declaring Shared Memory Arrays
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
__shared__ float subTileM[TILE_WIDTH][TILE_WIDTH];
__shared__ float subTileN[TILE_WIDTH][TILE_WIDTH];

## Slide 9: Shared Memory Tiling Basic Idea
Thread 1
Thread 2
…
in
Global Memory
Thread 1
Thread 2
…
Global Memory
in
On-chip Memory

## Slide 10: Outline of Technique
Identify a tile of global data that are accessed by multiple threads
Load the tile from global memory into on-chip memory
Have the multiple threads to access their data from the on-chip memory
Move on to the next block/tile

## Slide 11: Idea: Place global memory data into Shared Memory for reuse
Each input element is used in claculating by WIDTH P elements.
Load each element into Shared Memory and have several threads use the local version to reduce the memory bandwidth
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
Row
Col

## Slide 12: Tiled Multiply
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Break up the execution of the kernel into phases so that the data accesses in each phase are focused on one subset (tile) of M and N

## Slide 13: Loading a Tile
All threads in a block participate
  Each thread loads one M element and one N element in basic tiling code
Assign the loaded element to each thread such that the accesses within each warp is coalesced (more later).

## Slide 14: Work for Block (0,0)
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
Shared Memory
Shared Memory

## Slide 15: Work for Block (0,0) Threads use shared memory data in step 0.
Shared Memory
Shared Memory
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1

## Slide 16: Work for Block (0,0) Threads use shared memory data in step 1.
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1

## Slide 17: Work for Block (0,0)
N3,0
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,3
M0,2
M1,2
M1,3
N2,1
N2,0
N1,3
Shared Memory
Shared Memory

## Slide 18: Work for Block (0,0) Threads use shared memory data in step 2.
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
SM
N3,0
M0,3
M0,2
M1,2
M1,3
N2,1
N2,0
N1,3

## Slide 19: Loading an Input Tile 0
M
N
P
TILE_WIDTH
Width
Width
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
Width
Width
Tile 0 2D indexing for each thread:
M[Row][tx]
N[ty][Col]
ty
tx

## Slide 20: Loading an Input Tile 1
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Accessing tile 1 in 2D indexing:
M[Row][1*TILE_WIDTH+tx]
N[1*TILE_WIDTH+ty][Col]

## Slide 21: Loading an Input Tile m
M
N
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
However, recall that M and N are dynamically allocated and can only use 1D indexing:
M[Row][m*TILE_WIDTH+tx]
M[Row*Width + m*TILE_WIDTH + tx]
N[m*TILE_WIDTH+ty][Col]
N[(m*TILE_WIDTH+ty) * Width + Col]
m
m

## Slide 22: Accessing a Tile
P
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
tx
0
1
TILE_WIDTH-1
2
ty
2
1
0
TILE_WIDTH-1
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
To perform the kth step of the product within the tile:
subTileM[ty][k]
subTileN[k][tx]
subTileM
subTileN

## Slide 23: Barrier Synchronization
An API function call in CUDA
  __syncthreads()
All threads in the same block must reach the __syncthreads() before any can move on
Best used to coordinate tiled algorithms
  To ensure that all elements of a tile are loaded
  To ensure that all elements of a tile are consumed

## Slide 24
…
Thread 0
Thread 1
Thread 2
Thread 3
Thread 4
…
Thread N-3
Thread N-2
Thread N-1
Time

## Slide 25: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
1. __shared__ float subTileM[TILE_WIDTH][TILE_WIDTH];
2. __shared__ float subTileN[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the P element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the M and N tiles required to compute the P element
// The code assumes that the Width is a multiple of TILE_WIDTH!
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Collaborative loading of M and N tiles into shared memory
9. subTileM[ty][tx] = M[Row*Width + m*TILE_WIDTH+tx];
subTileN[ty][tx] = N[(m*TILE_WIDTH+ty)*Width+Col];
__syncthreads();
12. for (int k = 0; k < TILE_WIDTH; ++k)
13. Pvalue += subTileM[ty][k] * subTileN[k][tx];
14. __syncthreads();
15. }
16. P[Row*Width+Col] = Pvalue;
}

## Slide 26: Compare with Basic MM Kernel
__global__ void MatrixMulKernel(float* M, float* N, float* P, int Width)
{
// Calculate the row index of the P element and M
int Row = blockIdx.y * blockDim.y + threadIdx.y;
// Calculate the column index of P and N
int Col = blockIdx.x * blockDim.x + threadIdx.x;
if ((Row < Width) && (Col < Width)) {
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += M[Row*Width+k] * N[k*Width+Col];
P[Row*Width+Col] = Pvalue;
}
}

## Slide 27: Shared Memory and Threading
Each SM in Maxwell has 64KB shared memory (48KB max per block)
  Shared memory size is implementation dependent!
  For TILE_WIDTH = 16, each thread block uses 2*256*4B = 2KB of shared memory.
    Shared memory can potentially support up to 32 active blocks
    The threads per SM constraint (2,048) will limit the number of blocks to 8
    This allows up to 8*512 = 4,096 pending loads. (2 per thread, 256 threads per block)
  TILE_WIDTH 32 would lead to 2*32*32*4B= 8KB shared memory usage per thread block,
    Shared memory can potentially support up to 8 active blocks
    The threads per SM constraint (2,048) will limit the number of blocks to 2
    This allows up to 2*2,048 = 4,096 pending loads (2 per thread, 1024 threads per block)

## Slide 28: Memory Bandwidth Consumption
Using 16x16 tiling, we reduce the global memory by a factor of 16
  Each operand is now used by 16 floating-point operations
  The 150GB/s bandwidth can now support (150/4)*16 = 600 GFLOPS!
Using 32x32 tiling, we reduce the global memory accesses by a factor of 32
  Each operand is now used by 32 floating-point operations
  The 150 GB/s bandwidth can now support (150/4)*32 = 1,200 GFLOPS!
  The memory bandwidth is no longer a limiting factor for performance!

## Slide 29: Device Query
Number of devices in the system
    int dev_count;
    cudaGetDeviceCount( &dev_count);
Capability of devices
    cudaDeviceProp dev_prop;
    for (i = 0; i < dev_count; i++) {
    cudaGetDeviceProperties( &dev_prop, i);
// decide if device has sufficient resources and capabilities
    }
cudaDeviceProp is a built-in C structure type
  dev_prop.dev_prop.maxThreadsPerBlock
  Dev_prop.sharedMemoryPerBlock
  …

## Slide 30: Any more questions? Read Chapter 4!