## Slide 1: ECE408/CS483/CSE408 Spring 2018 Applied Parallel Programming Lecture 7-8: Convolution, Constant Memory and Constant Caching

## Slide 2: Objective
To learn convolution, an important parallel computation pattern
  Widely used in signal, image and video processing
  Foundational to stencil computation used in many science and engineering applications
  Critical component of Neural Networks and Deep Learning
Important techniques
  Taking advantage of cache memories

## Slide 3: Convolution Applications
A popular array operation that is used in various forms in signal processing, digital recording, image processing, video processing, computer vision, and machine learning.
Convolution is often performed as a filter that transforms signals and pixels into more desirable values.
  Some filters smooth out the signal values so that one can see the big-picture trend
  Others like Gaussian filters can be used to sharpen boundaries and edges of objects in images..

## Slide 4: Convolution Computation
An array operation where each output data element is a weighted sum of a collection of neighboring input elements
The weights used in the weighted sum calculation are defined by an input mask array, commonly referred to as the convolution kernel
  we will refer to these mask arrays as convolution masks or convolution filters to avoid confusion.
  The same convolution mask is typically used for all elements of the array.

## Slide 5: 1D Convolution Example
Commonly used for audio processing
  Mask_Width is usually an odd number of elements for symmetry (5 in this example)
  Mask_Radius is the number of elements used in convolution on each side of the pixel being calculated (2 in this example).
Calculation of P[2]:
3
4
5
4
3
3
8
15
16
15
N[0]
P
3
8
57
16
15
1
2
3
4
5
6
7
3
3
N[3]
N[1]
N[2]
N[5]
N[4]
N[6]
M[0]
M[3]
M[1]
M[2]
M[4]
P[0]
P[3]
P[1]
P[2]
P[5]
P[4]
P[6]
N
M

## Slide 6: 1D Convolution Example - more on inside elements
3
4
5
4
3
6
12
20
20
18
N[0]
P
3
8
57
76
15
1
2
3
4
5
6
7
3
3
N[3]
N[1]
N[2]
N[5]
N[4]
N[6]
M[0]
M[3]
M[1]
M[2]
M[4]
P[0]
P[3]
P[1]
P[2]
P[5]
P[4]
P[6]
N
M
Calculation of P[3]

## Slide 7: 1D Convolution Boundary Condition
3
4
5
4
3
0
4
10
12
12
M
N
P
3
38
57
16
15
1
2
3
4
5
6
7
3
3
0
N[0]
N[3]
N[1]
N[2]
N[5]
N[4]
N[6]
Filled in
M[0]
M[3]
M[1]
M[2]
M[4]
P[0]
P[3]
P[1]
P[2]
P[5]
P[4]
P[6]
Calculation of output elements near the boundaries (beginning and end) of the input array need to deal with “ghost” elements
  Different policies (0, replicates of boundary values, etc.)

## Slide 8: A 1D Convolution Kernel with Boundary Condition Handling
__global__ void convolution_1D_basic_kernel(float *N, float *M, float *P,
int Mask_Width, int Width) {
int i = blockIdx.x*blockDim.x + threadIdx.x;
float Pvalue = 0;
int N_start_point = i - (Mask_Width/2);
for (int j = 0; j < Mask_Width; j++) {
if (N_start_point + j >= 0 && N_start_point + j < Width) {
Pvalue += N[N_start_point + j]*M[j];
}
}
P[i] = Pvalue;
}
This kernel forces all elements outside the valid data index range to 0

## Slide 9: 2D Convolution
1
2
3
2
1
2
3
4
3
2
3
4
5
4
3
2
3
4
3
2
1
2
3
2
1
1
4
9
8
5
4
9
16
15
12
9
16
25
24
21
8
15
24
21
16
5
12
21
16
5
M
N
P
1
2
3
4
5
6
7
2
3
4
5
6
7
8
3
4
5
6
7
8
9
4
5
6
7
8
5
6
5
6
7
8
5
6
7
6
7
8
9
0
1
2
7
8
9
0
1
2
3
1
2
3
4
5
2
3
4
5
6
3
4
321
6
7
4
5
6
7
8
5
6
7
8
5

## Slide 10: 2D Convolution Boundary Condition
1
2
3
2
1
2
3
4
3
2
3
4
5
4
3
2
3
4
3
2
1
2
3
2
1
0
0
0
0
0
0
0
4
6
6
0
0
10
12
12
0
0
12
12
10
0
0
12
10
6
M
N
P
1
2
3
4
5
6
7
2
3
4
5
6
7
8
3
4
5
6
7
8
9
5
6
7
8
5
6
5
6
7
8
5
6
7
6
7
8
9
0
1
2
7
8
9
0
1
2
3
1
2
3
4
5
112
3
4
5
6
3
4
5
6
7
4
5
6
7
8
5
6
7
8
5
4

## Slide 11: 2D Convolution – Ghost Cells
0
0
0
0
0
0
3
4
5
6
0
2
3
4
5
0
3
5
6
7
0
1
1
3
1
1
2
3
2
1
2
3
4
3
2
3
4
5
4
3
2
3
4
3
2
1
2
3
2
1
0
0
0
0
0
0
9
16
15
12
0
8
15
16
15
0
9
20
18
14
0
2
3
6
1
179
0
ghost cells
(apron cells, halo cells)
M
N
P

## Slide 12: Access Pattern for M
Elements of M are called mask (kernel, filter) coefficients (weights)
  Calculation of all output P elements needs M
  M is not changed during grid execution
Bonus - M elements are accessed in the same order when calculating all P elements
M is a good candidate for Constant Memory

## Slide 13: Programmer View of CUDA Memories (Review)
Each thread can:
  Read/write per-thread registers (~1 cycle)
  Read/write per-block shared memory (~5 cycles)
  Read/write per-grid global memory (~500 cycles)
  Read/only per-grid constant memory (~5 cycles with caching)
Grid
Global Memory
Block (0, 0)
Shared Memory/L1 cache
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory/L1 cache
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 14: Memory Hierarchies
Review: If we had to go to global memory to access data all the time, the execution speed of GPUs would be limited by the global memory bandwidth
  We saw the use of shared memory (scratchpad) in tiled matrix multiplication.
Another important solution: Caches
Notes: Use backpack analogy

## Slide 15: Cache - Cont’d
A cache is an “array” of cache lines
  A cache line can usually hold data from several consecutive memory addresses
When data is requested from the global memory, an entire cache line that includes the data being accessed is loaded into the cache, in an attempt to reduce global memory requests
  The data in the cache is a “copy” of the original data in global memory
  Additional hardware is used to remember the addresses of the data in the cache line
Notes: Cache is transparent vs scratchpad which isn’t

## Slide 16: Caches - Cont’d
Some definitions:
  Spatial locality: when the data elements stored in consecutive memory locations are accessed consecutively
  Temporal locality: when the same data element is accessed multiple times in short period of time
Both spatial locality and temporal locality improve the performance of caches

## Slide 17: Scratchpad vs. Cache
Scratchpad (shared memory in CUDA) is another type of temporary storage used to relieve main memory contention.
  In terms of distance from the SMs, scratchpad is similar to L1 cache.
Unlike cache, scratchpad does not necessarily hold a copy of data that is also in main memory
  Scratchpad requires explicit data transfer instructions into locations in the scratchpad , whereas cache doesn’t

## Slide 18: Constant Cache in GPUs
Modification to cached data needs to be (eventually) reflected back to the original data in global memory
  Requires logic to track the modified status, etc.
Constant cache is a special cache for constant data that will not be modified during kernel execution by a grid
  Data declared in the constant memory will not be modified during kernel execution.
  Constant cache can be accessed with higher throughput than L1 cache for some common patterns

## Slide 19: How to Use Constant Memory
Host code allocates, initializes variables the same way as any other variables that need to be copied to the device
Use cudaMemcpyToSymbol(dest, src, size) to copy the variable into the device memory
This copy function tells the device that the variable will not be modified by the kernel and can be safely cached.

## Slide 20: Some Header File Stuff for M
#define MASK_WIDTH 5
// Matrix Structure declaration
typedef struct {
unsigned int width;
unsigned int height;
unsigned int pitch;
float* elements;
} Matrix;

## Slide 21: AllocateMatrix
// Allocate a device matrix of dimensions height*width
// If init == 0, initialize to all zeroes.
// If init == 1, perform random initialization.
// If init == 2, initialize matrix parameters, but do not allocate memory
Matrix AllocateMatrix(int height, int width, int init)
{
Matrix M;
M.width = M.pitch = width;
M.height = height;
int size = M.width * M.height;
M.elements = NULL;

## Slide 22: AllocateMatrix() (Cont.)
// don't allocate memory on option 2
if(init == 2) return M;
int size = height * width;
M.elements = (float*) malloc(size*sizeof(float));
for(unsigned int i = 0; i < M.height * M.width; i++)
{
M.elements[i] = (init == 0) ? (0.0f) :
(rand() / (float)RAND_MAX);
if(rand() % 2) M.elements[i] = - M.elements[i]
}
return M;
}

## Slide 23: Host Code
// global variable, outside any kernel/function
__constant__ float Mc[MASK_WIDTH][MASK_WIDTH];
…
// allocate N, P, initialize N elements, copy N to Nd
Matrix M;
M = AllocateMatrix(MASK_WIDTH, MASK_WIDTH, 1);
// initialize M elements
….
cudaMemcpyToSymbol(Mc, M.elements,
MASK_WIDTH*MASK_WIDTH*sizeof(float));
ConvolutionKernel<<<dimGrid, dimBlock>>>(Nd, Pd);

## Slide 24: Any MORE QUESTIONS? Read Chapter 7